## Slide 1
Z1
Z2
Z3
Z4
Z5
Z6
Z7
Z8
ZONE TEMPERATURE PROFILE
RHF-1 · WALKING BEAM REHEATING FURNACE · 8 ZONES · 40m
FURNACE SETPOINT
OPTIMISATION
AI-DRIVEN ADVISORY SYSTEM FOR RHF-1 · HAZIRA HSM
Transforming reactive setpoint management into data-driven,
anticipatory optimisation — powered by 30,731 slab records.
30,731
Slab records
analysed
R²=0.61
FCE prediction
accuracy
3–5%
Fuel saving
identified
₹3–8Cr
Annual saving
potential
CAPGEMINI INVENT · AM/NS INDIA — HAZIRA FACILITY · COMMERCIAL IN CONFIDENCE · APRIL 2026

## Slide 2
PROPOSAL AGENDA
What We Will Cover Today
01
Executive Summary
Strategic context, value proposition & key commitments
02
Current State Understanding
How RHF-1 operates today — data, fuel, and FCE patterns
03
High-Level Process Mapping
End-to-end slab journey through all 8 furnace zones
04
Challenges Identified
Root causes, quantified waste, and risk of inaction
05
Scope of Work (Refined)
Precise boundaries, assumptions, and phased deliverables
06
Our Vision & Solution
AI architecture, FCE model, and optimisation engine
07
Approach & Methodology
Phase-by-phase delivery, governance, and success metrics
DELIVERING MEASURABLE
FUEL SAVINGS FROM DAY ONE
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
2

## Slide 3
01 · EXECUTIVE SUMMARY
Why This Programme — And Why Now
The Problem
RHF-1 is running 10–19°C above recipe FCE targets across representative production schedules. 52–88 slabs per schedule are over-heated. Z1/Z2 preheat zones are consuming 38–55°C more heat than required.
Our Solution
An AI advisory system — trained on 30,731 slab records — predicts FCE dropout temperature per slab in real time and recommends the minimum-energy zone setpoints to achieve quality targets.
The Value
₹3–8 Crore per year in fuel savings through setpoint reduction of 22–55°C in preheat zones. Model validated at R²=0.61, MAE ±5.23°C. Payback in under 12 months.
OUR FOUR COMMITMENTS TO AM/NS INDIA
1
Model Live in 4 Months
FCE prediction model validated and advisory dashboard deployed within 4 months of data access.
2
Savings Proven in 6 Months
A/B validated fuel saving measurement delivered against agreed KPI baseline.
3
Operator Adoption
Every operator trained; recommendation acceptance rate ≥70% by Month 6.
4
Full Knowledge Transfer
Complete model documentation, code, and governance framework handed over at programme close.
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
3

## Slide 4
02 · CURRENT STATE UNDERSTANDING
How RHF-1 Operates Today
DATA FOUNDATION
30,731
Slab records (Aug–Dec 2025)
4,344
Hourly process readings
8
Zone temperature channels
5
Representative schedules analysed
FCE MEAN DEVIATION BY SCHEDULE (°C above recipe)
S1
+19.1°C
S2
+5.9°C
S3
+8.9°C
S4
+17.7°C
S5
+12.7°C
ZONE FUEL SLOPES (Nm³/hr per °C)
Z3 Heating
40.76
Z2 Preheat
34.14
Z1 Preheat
25.77
Z4 Heating
14.2
Z5–Z8 Soak
1.56
Static Setpoints
Zone SPs are set once per grade and not adjusted for slab thickness, width, or entry temperature. A 220mm cold slab charged at 80°C gets the same setpoint as a 200mm warm slab at 350°C.
No FCE Visibility
Operators cannot predict FCE dropout temperature before the slab is discharged. All intervention is reactive — by which time the slab has already over-heated and fuel has been consumed.
Preheat Over-serving
Z1 and Z2 are running 38–55°C above the model-optimal setpoint in severe schedules. Z3 alone costs 40.76 Nm³/hr per extra °C. This is the single largest identified waste lever.
Coffin Slab Blind Spot
Coffin slabs (hollow core) require an extra 8.2°C FCE compensation and +8 minutes soaking. Currently, no system flags or compensates for coffin loading — each event is managed by operator memory.
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
4

## Slide 5
03 · HIGH-LEVEL PROCESS MAPPING
End-to-End Slab Journey Through RHF-1
Z1 PREHEAT
1238°
actual
SP 1260°
25.8 Nm³/°C
Z2 PREHEAT
1239°
actual
SP 1265°
34.1 Nm³/°C
Z3 HEATING
1314°
actual
SP 1320°
40.8 Nm³/°C
Z4 HEATING
1306°
actual
SP 1315°
14.2 Nm³/°C
Z5 SOAKING
1244°
actual
SP 1260°
1.6 Nm³/°C
Z6 SOAKING
1244°
actual
SP 1258°
0.7 Nm³/°C
Z7 SOAKING
1245°
actual
SP 1258°
1.0 Nm³/°C
Z8 DISCHARGE
1240°
actual
SP 1255°
0.5 Nm³/°C
IN
OUT
DATA & AI LAYER
SCADA / DCS
Zone temps, fuel flows
real-time @1Hz
L2 MES
Slab schedule: grade
thickness, width, order
FEATURE ENG.
Dwell time, mass flux
entry temp delta
FCE MODEL
R²=0.61 · MAE ±5.23°C
30,731 slab records
OPTIMISATION
Min-energy SPs
OEM envelope enforced
ADVISORY
Zone SPs + saving
Confidence score
OPERATOR
Accept/Modify/Reject
Logged & measured
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
5

## Slide 6
04 · CHALLENGES IDENTIFIED THROUGH ASSESSMENT
What the Data Reveals — Root Causes & Waste
+14.3°C
Average FCE excess
across all 5 schedules
292
Overheated slabs per
5-schedule sample
~1,176
Nm³/hr fuel waste
identifiable & avoidable
₹5Cr+
Annual saving
opportunity at stake
C1
No Speed/Dimension Compensation
Zone SPs are static recipes. Slab thickness (200–235mm), width (1040–1700mm) and entry temp (25–450°C) vary continuously but setpoints do not adapt. The same SP serves a cold 235mm slab and a warm 200mm slab — producing systematic FCE deviation.
⚡ ±15°C FCE swing between cold-thick and warm-thin slabs at identical SP
C2
Z1/Z2 Systematic Over-Firing
Preheat zones (Z1, Z2) are the highest fuel-per-°C zones outside Z3. In severe schedules they run 38–55°C above the model optimum. Z1 saves 25.77 Nm³/hr per °C reduction; Z2 saves 34.14 Nm³/hr. Combined preheat waste is the largest single saving lever.
⚡ ~500–900 Nm³/hr excess fuel attributable to preheat over-serving alone
C3
Z6 Model Coefficient Sign Error
The legacy prototype model had Z6 with a NEGATIVE FCE coefficient (−0.007) — implying raising Z6 SP reduces FCE. The schedule model fitted on actual measured temperatures shows Z6 is POSITIVE (+0.013). Incorrect sign leads to wrong advisory direction for soaking zone management.
⚡ Advisory recommendations systematically biased in soaking zone optimisation
C4
Recipe Transition FCE Steps
When recipe target increases between consecutive slabs (e.g. 1220→1230°C), the recommended zone temperatures step up immediately — causing thermal shock and PLC hunting. No gradual ramp logic exists in the current operation, producing FCE excursions during every recipe change.
⚡ FCE spike of 3–8°C at every recipe transition; upstream quality risk
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
6

## Slide 7
05 · SCOPE OF WORK — REFINED
Precisely What We Will Deliver — And What We Will Not
✓ IN SCOPE
• FCE dropout temperature prediction model (all 8 zones, R²≥0.61 target)
• Zone setpoint optimisation engine — minimum energy, OEM constraints enforced
• Gradual FCE ramp logic across recipe target transitions (3-slab window)
• Per-zone energy quantification: E = (COREX / 5.12) + NG per zone
• Coffin slab detection and FCE compensation (−8.2°C model adjustment)
• Operator advisory dashboard — live FCE prediction, zone bars, SP recommendations
• Accept / Modify / Reject workflow with full audit trail and operator logging
• OT-to-IT data pipeline (AM/NS India provides access; Capgemini builds pipeline)
• Model governance framework, monthly performance reviews, retraining protocol
• Operator and supervisor training + full knowledge transfer at programme close
✕ OUT OF SCOPE
✕ Any furnace other than RHF-1
✕ PLC write-back / closed-loop control (Phase 2)
✕ Rolling mill downstream optimisation
✕ ERP / SAP integration
✕ Surface defect quality inspection
✕ Refractory condition monitoring
⚠ KEY ASSUMPTIONS
→ OT read access within 4 weeks of kick-off
→ Min. 6 months historical data available
→ 8-zone configuration unchanged during delivery
→ 2 operators + 1 SM available for UAT (Month 5–6)
PHASES
0
Foundation
M1–2 · Data Pipeline Live
1
Model Build
M3–4 · Model Validated
2
Advisory Live
M5–6 · Dashboard Go-Live
3
Optimisation
M7–8 · Savings Validated
4
Handover
M9 · Full Handover
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
7

## Slide 8
06 · SOLUTION — OUR VISION
The Intelligent Furnace Advisor
Every slab that enters RHF-1 exits at exactly the right temperature — no hotter, no cooler — using the minimum fuel required. Our AI advisor makes every operator as effective as the plant's best operator, on every shift, every day.
AI MODEL ARCHITECTURE
INPUT
· Slab: grade, thickness, width
· Entry temperature (°C)
· Zone temps Z1–Z8 (actual)
· COREX + NG flows per zone
· L2 MES next-slab schedule
· Coffin slab flag
FEATURES
· Dwell time per zone
· Mass flux (thk × width)
· Entry temp delta
· Thermal inertia windows
· Grade-change lag flags
· Energy = (COREX/5.12)+NG
FCE MODEL
· R² = 0.6088
· MAE ± 5.23°C
· n = 30,731 slabs
· Zone-weighted regression
· Trained on ACTUAL temps
· Fixed SP offset correction
OUTPUT
· FCE dropout prediction
· Zone: OK/Over/Under
· 8 zone setpoints
· Confidence score
· Nm³/hr saving per zone
· Explanation (top-3 factors)
ADVISORY DASHBOARD PANELS
KPI Strip
Live fuel, FCE avg, overheated slab count, shift SFC vs target — always visible, RAG-coded
Zone Status Bars
8 vertical bars: SP vs actual vs AI-predicted impact. Green/amber/red per zone. Refreshes ≤90s
Recommendation Panel
Recommended SP per zone · Delta from current · Confidence score · Nm³/hr saving · One-click Accept/Modify/Reject
FCE Prediction Table
Per-slab FCE prediction · Recipe target · Deviation · Heat-path mini-bars across 8 zones · Updates on every slider move
Slab Queue Viewer
All slabs in queue · Grade · Entry temp · Predicted FCE · Zone position · Coffin flag · Status dot colour
Energy Progress Bar
Current fuel vs P25 efficient baseline · Optimal marker · Potential Nm³/hr saving — live as operator adjusts SPs
WHY OUR APPROACH IS DIFFERENT
★ Schedule model fitted on ACTUAL zone temps — not SP-derived proxies — giving 161°C more accurate intercept
★ Gradual 3-slab FCE ramp prevents thermal shocks at recipe transitions — unique to this implementation
★ Z6 sign-flip corrected: positive soaking coefficient (+0.013) properly included in advisory boost logic
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
8

## Slide 9
07 · APPROACH & METHODOLOGY
How We Will Deliver — Phase by Phase
PHASE 0
Months 1–2
FOUNDATION
→ OT data pipeline build
→ SCADA historian connect
→ Data quality audit
→ Architecture sign-off
→ Baseline KPI freeze
M1: Data Pipeline Live
PHASE 1
Months 3–4
MODEL BUILD
→ FCE regression model
→ Zone coefficient calibration
→ Optimisation engine
→ Deviation classifier
→ Feature engineering
M2: Model Validated
PHASE 2
Months 5–6
ADVISORY LIVE
→ Dashboard deployment
→ Accept/Modify/Reject UI
→ Operator training
→ Feedback collection
→ Shadow-mode validation
M3: Dashboard Go-Live
PHASE 3
Months 7–8
OPTIMISATION
→ A/B performance test
→ Model recalibration
→ Savings measurement
→ Phase 2 readiness
→ Governance handover
M4: Savings Validated
PHASE 4
Month 9
HANDOVER
→ Knowledge transfer
→ Full documentation
→ Support model live
→ PSC close-out
→ Phase 2 scoping
M5: Full Handover
GOVERNANCE MODEL
Programme Steering (PSC)
VP Ops + Capgemini MD
Quarterly
Project Mgmt (PMC)
AM/NS PM + Capgemini PM
Bi-weekly
Model Governance Board
Process Eng + DS Team
Monthly
SUCCESS METRICS
✓ FCE prediction accuracy
R² ≥ 0.60, MAE ≤ ±6°C on held-out data
✓ Alert precision
< 1 false alarm per 10 alerts (Type I < 10%)
✓ Alert recall
< 5% true deviations missed (Type II < 5%)
✓ Fuel saving
≥ 3% SFC reduction vs baseline, A/B validated
✓ Adoption rate
≥ 70% recommendations accepted by Month 6
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
9

## Slide 10
NEXT STEPS
Let's Begin
This Journey Together
01
Proposal Alignment
Review scope, timeline, and commercial terms. Target: agreement within 2 weeks.
02
Kick-off Meeting
Joint session with AM/NS IT, Process Eng, and Capgemini team. Agree data access plan.
03
OT Data Access
AM/NS India IT provides SCADA historian and L2 MES read access within 4 weeks.
04
Phase 0 Begin
Capgemini builds data pipeline. Data quality audit completed. Architecture signed off.
OUR COMMITMENT TO AM/NS INDIA
A programme built on facts,
not promises.
30,731
Slab records already analysed — model coefficients validated
R²=0.61
FCE prediction model accuracy demonstrated on real Hazira data
5 Schedules
Covering S1–S5, Aug–Dec 2025, proving consistent over-heating pattern
₹3–8Cr
Annual saving estimate grounded in actual zone fuel slopes and FCE deviations
CAPGEMINI INVENT
RHF-1 Furnace Setpoint Optimisation · AM/NS India, Hazira
Programme Director · Lead Data Scientist · Solution Architect
COMMERCIAL IN CONFIDENCE · APRIL 2026
CAPGEMINI INVENT · RHF-1 SETPOINT OPTIMISATION
10